## Slide 1: Automotive Systems – Perception and situation understanding Simulative Robot Detection with different sensors and Kalman-filter
Prof. Dr.-Ing. Raoul Zöllner
Johannes Buyer, M. Eng.
lgerstla@stud.hs-heilbronn.de, jkurz1@stud.hs-heilbronn.de

## Slide 2: Problem description
Observation of Robots in a room
Two Cameras with limited Field of View
One Lidar with low angular resolution
Only position measurable
Known state Equation of robots

## Slide 3: Boundary conditions
Room Size 2D = [40 m, 30 m]
Cameras
  Located in the upper two corners of the room
  FOV of 40.0 degrees
  Measures position in x and y
  Normally distributed uncertainty with sigma of 0.2
Lidar
  Located in the lower middle of the room
  Angular resolution of 10 degrees
  Measures distance to robot and angle of hitten beam
  Normally distributed uncertainty of distance with sigma of 0.2, angular sigma 0.1

## Slide 4: Boundary conditions
Robots
  Differential drive  direction of velocity is orientation of robot
  One step every 100 ms
    0.3 m movement per step
    Change of direction randomly between -0.2 and 0.2 per step
  Every three seconds change of direction randomly between 0 and
  Reflection from the walls

## Slide 5: Visualization of room, Sensors and robots

## Slide 6: Chosen solution approach
Multi Target Tracking with Mahalanobis distance-based data association
Extended Kalman-Filer
https://www.kalmanfilter.net/img/summary/KalmanFilterDiagram.png

## Slide 7: Sensor Clustering with DBSCAN – Mathematical Context & Implementation
Purpose: Reduce noisy detections by clustering nearby sensor data (camera & LiDAR).
Algorithm: DBSCAN groups detections based on ε-radius proximity and point density.
Mathematical basis: Points form clusters if within ε-distance and satisfy minPts.
Centroid computation: For each cluster , the centroid ​ is used as a proxy measurement.
Implementation: cluster_measurements() filters outliers (label = -1), returns only valid cluster centers.
Impact: Significantly reduces input dimensionality and improves assignment stability.

## Slide 8: Mahalanobis Distance & Multi-Target Data Association
Goal: Assign clustered measurements to EKF tracks based on statistical compatibility.
Mahalanobis distance: , mit
Assignment logic: Cost matrix built from all EKF–cluster pairs using Mahalanobis distances.
Optimization: Hungarian Algorithm solves linear sum assignment for minimal total distance.
Fallbacks: Unassigned tracks receive nearest valid measurement under relaxed threshold.

## Slide 9: State vector, measurement vector
State vector:
Input vector:
Measurement vector:

## Slide 10: Motion / Transition Model
System dynamics function

## Slide 11: Measurement Model
Measurement function:

## Slide 12: Jacobi-matrices
System matrix:
Measurement matrix:

## Slide 13: Parameterization of the filter
Process noise covariance:
Measurement noise covariance:
Error covariance matrix:

## Slide 14: observability
Observability at state :
Observability matrix :
Observability matrix rank:  System observable

## Slide 15: Structure of the implemented program
Implementation in ROS2 Nodes
  robotControllerNode  Simulation of roboter movement
  *DetectionNode  Simulation of detection with added noise
  ekfNode  extended Kalman-Filter
  visualizationNode  Visualization of room, roboters, sensors, covariance

## Slide 16: performed experiments and results

## Slide 17: Literature

## Slide 18: Thank you for your attention